## Slide 1: DATA SCIENCE LAB.3 FINAL PROJECT
Aggelos Tako, Anastasia Zafeiriou, Anna Dosiou, Konstantinos Christou

## Slide 2: CEMENT MILL PROCESS
The Cement Mill grinds the hard, nodular clinker from the cement kiln into the fine grey powder that is cement. This cement mill produces two types of cement.
The production process is separated into two blocks. Those are the Separator Motor Block and the Mill Differential Pressure Block. There are given data for 6 months, from May to October.

## Slide 3: TYPES OF PORTLAND CEMENT
Pro
Composition: clinker, gypsum, pozzolanic materials
Durability: pozzolanic  chemical attacksꜜ, heat of hydrationꜜ, workabilityꜛ
Environmental Impact: carbon footprintꜜ, greenhouse gas emissionsꜜ, conserving natural resourcesꜛ
CPII
Premium
Composition: clinker, gypsum, supplementary cementitious materials (SCMs)
Durability: SCMs  risk of crackingꜜ, strengthꜛ, chemical, sulfate attacksꜜ, alkali-silica reactionsꜜ
Environmental Impact: CO2ꜜ, reliance on virgin raw materialsꜜ
CPIV

## Slide 4: CEMENT MILL BLOCKS
Separator Motor
Separator Speed
Mill Differential Pressure
Mill Differential Pressure
Total Feed
Bucket Elevator
Fly Ash 1,2
Fan Speed
Separator Speed
Grinding Pressure
Mill Water Injection

## Slide 5: Challenges of the datasets
Data Type (e.g. Date/Time, Integer/Float)
Separation of Smooth Motor Operation
Errors, NaN Values, Time Gaps
Time Delay between Timeseries
Duplicate Columns

## Slide 6: Block 1: Separator Motor Block
Predicted with LSTM
Train / Test Set: 80 / 20 %
Performance
RMSE: 0.459 MAPE: 0.006 R^2: 0.832 MAE: 0.357

## Slide 7: Cleaning and Preprocessing
Handling Missing Data and Errors
Merging Duplicate Columns (e.g. gypsum, total feed)
Defining proper date / time format
Converting Data Types

## Slide 8: Exploratory Data Analysis (EDA)
Distribution of Mill Motor Operation (KW) – Normal Operation

## Slide 9: Exploratory Data Analysis (EDA)
Mill Motor Timeseries
Interrupted operation in the first months
After possible maintaining process the mill is operating in a higher power level
Separator Motor (KW)

## Slide 10: Exploratory Data Analysis (EDA)
Distribution of Separator Motor (KW) per Cement Type

## Slide 11: Exploratory Data Analysis (EDA)
Correlations

## Slide 12: Block 1: Separator Motor Block
Predicted with LSTM
Inputs: Separator Speed, Mill DP
Performance
RMSE: 1.293 MAPE: 0.0138 R^2: 0.230
Predicted with LSTM
Inputs: Separator Speed, Mill DP, Cement Type
Performance
RMSE: 1.283 MAPE: 0.013 R^2: 0.242 MAE: 0.785
Predicted with LSTM
Inputs: Separator Speed, Mill DP, Cement Type, Gypsum
Performance
RMSE: 0.949 MAPE: 0.006 R^2: 0.585 MAE: 0.385

## Slide 13: Block 1: Separator Motor Block
Predicted with LSTM
Performance
RMSE: 0.459 MAPE: 0.006 R^2: 0.832 MAE: 0.357
Predicted with Random Forest
Performance
RMSE: 1.025 MAPE: 0.013 R^2: 0.162 MAE: 0.793
Machine Learning
Deep Learning

## Slide 14: Block 2: Mill Differential Pressure Block
Inputs variables:
'total_feed_ton/h_pv_NEW',’
grinding_pressure_bar_pv’,
'separator_speed_rpm_pv’
Random Forest

## Slide 15: Block 2: Mill Differential Pressure Block
Predicted with Random Forest
Performance
Mean Squared Error: 10.5455
Mean Absolute Error: 2.390
R-squared Score: 0.393
Machine Learning
Predicted with Random Forest
Performance
Mean Squared Error: 10.251
Mean Absolute Error: 2.344
R-squared Score: 0.390
Input variables: total_feed, fly_ash_2, fly_ash_1, grinding_pressure, mill_injection_water, bucket_elv_mtr, separator_speed

## Slide 16: Suggestions for model improvement Time Delay – DTW, Correlation Matrix 01 Model Training with Time breaks 02 Timeseries Smoothing - Reduce Noise 03 NN Model in Block 2 04

## Slide 17: Thank you!